## Slide 1
UNSUPERVISED MACHINE LEARNING-BASED USER CLUSTERING IN THZ-NOMA SYSTEMS
TEAM:
ABHINAV DESHPANDE (IMT2022580)
AJITESH KUMAR SINGH (IMT2022580)
ML FOR WIRELESS COMMUNICATION

## Slide 2
TABLE OF CONTENTS
  Problem Statement
  System Modelling and Beamforming
  Problem definition
  K-means
  DBSCAN
  AHC
  Results obtained
  Timeline Diagram

## Slide 3
Keep it or delete it!
Same
PROBLEM STATEMENT
6G Communication Need:
  5G networks cannot meet future demands (ultra-high throughput, massive connectivity, ultra-low latency).
THz-NOMA as a Solution:
  Terahertz (THz) spectrum offers ultra high bandwidth for communication.
  Non-Orthogonal Multiple Access (NOMA) enhances spectral efficiency by allowing multiple users to share bandwidth.
Key Challenge:
  Efficient user clustering in THz-NOMA networks without predefined cluster numbers.

## Slide 4
THz-NOMA System Model
P. User
S. User
h1
h2
B.S.
  Primary User: Higher priority users with stronger channel.
  Secondary User: Lower priority users with weaker channel
h1 > h2
p1 < p2
NOMA: Non-orthogonal Multiple access. Transmit for entire time but assign different powers to users.
NOMA has 2 kind of users:
Treated as noise
Successive Interference Cancellation (SIC)
Term of interest
Direct Decoding at S. User
SIC and then Decoding at P. User

## Slide 5
WHY CLUSTERING ?
Same
Adaptive Resource Allocation
The THz spectrum is highly sensitive to attenuation and environmental factors. Clustering enables adaptive and automatic grouping of users based on spatial and signal characteristics.
The Base Station Starts Beamforming
BS : L antennas
Users : N
  It cannot assign a dedicated beam to each user, so it has to group them into clusters.
  Each cluster is assigned a beam, with one Primary User leading the group
Without Clustering : Some users end up in beams that don’t match their spatial positions, leading to signal distortion and packet loss.

## Slide 6
Same
Signal vector sent from B.S.
to primary user
Keep it or delete it!
BEAMFORMING
Hybrid beamforming (analog and digital combined) for primary users.
Analog Beamforming vector
Digital beamforming matrix
AOD (angle of departure)

## Slide 7
Same
Keep it or delete it!
Constraints:
1. Each user should be assigned to a single cluster. (P1-b)
2. Total power of all secondary users ≤ total BS power. (P1-c)
3. Primary user data rate ≥ minimum QoS requirement. (P1-d)
PROBLEM DEFINITION
Goal: Maximize the sum of data rates for all secondary users.
Optimisation Problem:

## Slide 8
Keep it or delete it!
PROPOSED USER CLUSTERING APPROACHES

## Slide 9
Keep it or delete it!
K-MEANS
Limitations:
  Uses a pre-defined number of clusters (k).
  Forces outliers into clusters.
  Sensitive to initial centroid selection
Group users based on AOD: Each secondary user (j) has an AOD value (aj) which is assigned to nearest centroid based on distance
Centroids are updated till the condition for stopping is achieved. (standard k-means approach)
We are going to use k-means as a benchmark for other proposed algorithms.
Angle of Departure

## Slide 10
Keep it or delete it!
Same
DBSCAN
Density-based spatial clustering application with noise
Algorithm:
  For all users (1 -> N):
    Start with an unvisited user. Check if it has atleast minPts neighbours in Epsilon neighbourhood.
    If yes (we call this dense enough), form a new cluster and expand it by adding reachable users.
    If no, label it as noise. (although this can be changed later)
Limitations:
  Hyperparameters: minPts, Epsilon need to be pre-configured.
Advantages over k-means:
  Determines K dynamically
  Labels outliers as noise

## Slide 11
Same
AHC

## Slide 12
Keep it or delete it!
Same
No Fixed Cluster Count
  Traditional clustering (e.g., K-Means) requires the number of clusters in advance.
  AHC automatically determines the number of clusters by progressively merging users based on similarity (e.g., AoD).
Adapts to User Distribution
  If users are closely spaced, AHC groups them into fewer clusters.
  If users are widely distributed, AHC creates more clusters dynamically.
Threshold-Based Merging
  AHC merges users step-by-step until a stopping criterion (e.g., sum rate maximization, minimum beam interference) is met.
  The system does not need prior knowledge of cluster count but learns it from the AoD distribution.
HOW IS AHC DYNAMIC

## Slide 13
Keep it or delete it!
Same
RESULTS OBTAINED

## Slide 14
Keep it or delete it!
Same
PLOTS
For L = 10(# of antennas at B.S.)
Link to our code base: https://github.com/Transyltooniaa/Unsupervised-Machine-Learning-Based-User-Clustering-in-THz-NOMA-Systems

## Slide 15
TIMELINE DIAGRAM

## Slide 16
THANK YOU

## Slide 17
QUESTIONS